## Slide 1
Practice 4: Half-Term Challenge
Autonomous Object Manipulation Pipeline
Tec de Monterrey Hello Robot KeyPrediction

## Slide 2
The Operational Goal
Build a complete, non-interventional state machine pipeline to detect, approach, and grab a target object.
3D Object Localization via depth sensing
Multi-phase sequential state architecture
Safe closing and payload lifting sequence
Tec de Monterrey KeyPrediction

## Slide 3
Incremental Script Architecture
p4_1_locate_object.py — Stationary 3D plotting
p4_2_approach.py — Navigation via Flank mode
p4_3_align.py — Fine wrist-camera tracking adjustments
p4_4_reach.py — Arm extension until target depth (~12 cm)
p4_5_grab.py — Closed gripper lifting execution
Hello Robot KeyPrediction

## Slide 4
Critical Control Conditions
Flank Approach
The robot presents its flank side rather than driving straight forward to clear visual blocks and ensure optimal mechanics.
Reach Threshold
Arm extension transitions precisely based on continuous distance updates until depth readings settle below 12 cm.
Tec de Monterrey Hello Robot

## Slide 5
Challenge Deliverables
Screen Capture + Voiceover Walkthrough
• Visible execution showing continuous transitions (Approach → Align → Reach → Grab)
• Operational explanation of 3D frame localization via forward kinematics
• Structural answer defining why the robot approaches via flank orientation
• Breakdown of the 3 transition rules required to initiate the grab sequence safely
Tec de Monterrey Hello Robot KeyPrediction