## Slide 1
Practice 2: Stretch Robot Kinematics
Velocity, States, and Command Blending
Tec de Monterrey Hello Robot KeyPrediction

## Slide 2
Environment Setup & Updates
1. Update Repository
Pull recent improvements. Warning: Overwrites local changes.
2. Sync Dependencies
Ensure packages match specifications securely:
Tec de Monterrey KeyPrediction

## Slide 3
Velocity Control & Joint States
Part 1: Velocity Control
Command normalized joint speeds via controller.set_velocities().
Task: Create p2_1_velocity.py to oscillate head pan using a sine wave:
Part 2: Reading State
Retrieve live position metrics with controller.get_state().
Task: Create p2_2_state.py to print joint frames dynamically (Linear = meters, Rotational = radians).
Hello Robot KeyPrediction

## Slide 4
Position Control & Input Devices
Part 3: Position Bouncing
Use StateController to generate targeted velocity adjustments natively.
Task: Make the arm bounce continuously between 0.1 m and 0.3 m in p2_3_position.py.
Part 4: Unified Inputs
The stretch_toolkit.input abstraction maps hardware universally.
• is_pressed("button"): Digital fallback • get_axis("RX"): Analog stick scaling • rising_edge("A"): One-shot frames
Tec de Monterrey Hello Robot

## Slide 5
Command Layering & Override
Proportional Blending
merge_proportional() combines manual and autonomous commands dynamically.
Under a 0.05 deadband, autonomy rules; outside it, human inputs smoothly blend and override.
The Y Toggle Mode
teleop.get_manual_override() manages full controls. Press Y / y to swap:
KeyPrediction Hello Robot

## Slide 6
Submission Checklist
Video File Requirements (30-60 Seconds)
Your video submission must clearly demonstrate:
1. Arm bouncing autonomously (0.1m to 0.3m)
2. Proportional human override during active bounce
3. Pressing Y key to transition into total MANUAL mode
4. Pressing Y again to resume target AUTONOMOUS loop
Tec de Monterrey Hello Robot KeyPrediction