## Slide 1
TECNOLÓGICO DE MONTERREY
Practice 1: Setting up the Stretch Robot Simulator
Robotics and Cyber-Physical Systems Lab

## Slide 2
Objectives & Requirements
Key Objectives
• Install and verify the MuJoCo base simulator
• Integrate RoboCasa kitchen environments
• Complete a block stacking teleop challenge
System Requirements
• Windows, macOS, or Linux
• uv package manager & Git
• 5+ GB free disk space

## Slide 3
Software Installation
Install uv: Use the PowerShell or curl script to get the fast package manager.
Clone Repository: Use --recurse-submodules to pull the digital twin assets.
Commands: git clone https://github.com/SilentSammy/stretch_mujoco_digital_twin
Sync: Run uv sync if you encounter startup errors.

## Slide 4
Verification: Base Sim
Launch Command
Run the teleoperation demo:
uv run teleop_demo.py
Expected Result: A MuJoCo viewer opens with the Stretch robot and two colored blocks (blue box & red cylinder).

## Slide 5
RoboCasa Kitchen
Install: Run the uv pip commands for robocasa and robosuite.
Assets: Note that kitchen assets are ~5GB.
Enable: Set "enabled": true in robocasa_config.json.

## Slide 6
Teleoperation & Controls
Base & Lift
WS: Forward/Back DA: Rotate ZX: Lift Up/Down
Arm & Wrist
VC: Extend/Retract L J K I U O: Wrist Yaw, Pitch, Roll
Gripper & Cam
MN: Open/Close 1-5: Toggle Camera Feeds (RGB/Depth)

## Slide 7
Evidence & Submission
Final Deliverables
1. Video Link: Demonstrating joint movements with explanations.
2. Screenshots: Kitchen environment (Part 2) and stacked blocks (Part 4).
3. Written Summary: 9 Degrees of Freedom (DOF) descriptions.

## Slide 8
Practice 1 Complete
Next Steps: Programmatic Control & Computer Vision
Resource: github.com/SilentSammy/stretch_mujoco_digital_twin

## Slide 9
Image Sources
https://yasunori.jp/assets/2024/mjcf/mujoco_article_cover.png
Source: yasunori.jp
https://the-decoder.com/wp-content/uploads/2024/05/RoboCasa-title-1200x675.png
Source: the-decoder.com
https://us.v-cdn.net/6038536/uploads/migrated/UDZWWD0WUQUK/11b7f7ce-3ec8-4aea-85f3-51ca86c47761.png
Source: community.instructure.com