## Slide 1
Practice 3: Visual Servoing
Closed-Loop Camera Feedback Control
Tec de Monterrey Hello Robot KeyPrediction

## Slide 2
Setup & Baseline Control
Repository Update
Ensure environment files match upstream changes securely:
git pull
uv sync
Part 1: Manual Control
Establish a manual control framework in p3_1_manual.py.
Map hardware velocities via:
teleop.get_normalized_velocities()
Tec de Monterrey KeyPrediction

## Slide 3
Vision Feeds & Color Segmentation
Part 2: Dual Camera Feeds
Open separate, live stream visualization windows inside p3_2_cameras.py:
• "RGB Camera" window
• "Depth Camera" window
Part 3: HSV Blue Mask
Isolate target tracking pixels inside p3_3_mask.py using HSV bounds:
cv2.inRange(hsv, lower, upper)
Displays blue targets as clean, isolated white blobs.
Hello Robot KeyPrediction

## Slide 4
Part 4: Closed-Loop Tracking
Object Centering Architecture (p3_4_servo.py)
1. Centroid: Locate target mass via cv2.findContours() and cv2.moments().
2. Error: Calculate pixel delta offset from the literal image center framework.
3. Control: Apply proportional scale adjustment gain (Kp = 0.5) to pan/tilt.
4. Blending: Blend manual inputs smoothly via merge_proportional().
Tec de Monterrey Hello Robot

## Slide 5
Submission Requirements
Screen Recording with Voiceover
• Simultaneous display of 3 windows (RGB, Depth, Blue Mask)
• Autonomous head tracking tracking a moving blue object
• Human operator manual override yielding seamlessly
• Oral walkthrough detailing HSV selection & proportional loops
Tec de Monterrey Hello Robot KeyPrediction